## Slide 1: Development Flow for Edge AI Devices
ML MODEL DEVELOPMENT (MLOps)
CLASSIC EMBEDDED DEVELOPMENT
Model searcher
Model Compressor
Trained
ML Model
Weight clustering
Quantization
Compile
Validate
Optimized ML Model
Arm tools integrate here
Data
Use-Case
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output Interface
SDS Data Capturing
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 2: Development Flow for Edge AI Devices
DATA STREAM
ML Input Data
Sensor
Audio
Video
Input Interface
Signal Conditioning
Optimized ML Model
Output Interface
SDS Recorder Interface
ML Output Data
SDS Recorder Interface
Physical Sensor Input Data
SDS Recorder Interface
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 3: SDS-Framework: Record Real-world Data and Playback to AVH
Semihosting Interface
MCU Device
Synchronous Data Stream (SDS) Transfer Interfaces
Sensor Interface (physical)
Sensor Interface
SDS Recorder Interface
IoT Socket Network Stack
SDSIO Server Running on Host
User Algorithm under Development
Synchronous Data Stream (SDS) Transfer Interfaces
SDS Playback Interface
User Algorithm under Development
Record physical sensor (real-world) data using MCU hardware
Playback real-world data for verification
SDS Data Files have multiple use cases:
Input for ML Algorithm development
Input for Filter Designers (i.e. ASN)
When capturing Algorithm outputs, validation for regression
SDS Interfaces can be based on
https://github.com/ARM-software/CMSIS-DSP/tree/main/ComputeGraph
Currently under development
https://github.com/RobertRostohar/SDS-Framework
Simplify Development of Embedded Applications that utilize DSP or ML algorithms with Sensor/Audio Input
Physical Sensor
Physical Sensor Input Data
Physical Sensor Input Data
MICROCONTROLLER HARDWARE
SIMULATION

## Slide 4: Development Flow for Edge AI Devices
DATA STREAM UNDER DEVELOPMENT
ML Input Data
Signal Conditioning
Optimized ML Model
Output
SDS Recorder
ML Output Data
Physical Sensor Input Data
SDS Player
SDSIO Server running on development host system
SDS INTERFACE LAYER
or
SDS Recorder
Notes: But how is such an Edge AI application developed? Let’s take a look.
An Edge AI Device has a classic embedded part that integrates an Optimized ML Model. The classic embedded software interfaces to the sensor, audio or video input of your device, and contains DSP algorithms for signal conditioning. And of course, the output interface.
For the ML Development you need real-world data. Arm offers the SDS software component for data capturing which we will demonstrate in a dedicated webinar later this year. The data is fed into the MLOps system and Edge Impulse is one of our partners in this space.
In the MLOps system, you specify your use-case, and a model searcher helps identifying the right model. Afterwards, compression, training, clustering, and quantization is applied to the model to fit it into the memory of constrained edge devices. Finally, this is compiled, validated, and delivered to the classic embedded development flow for integration.
Edge Impulse will now show us how this works in practice with their system. Over to you Alessandro!

## Slide 5: SDS: flexible stream management for sensor and audio data
Supports the whole development cycle: data recording, analysis, ML training, playback
X         
Y         
Z         
t
SDS Metadata File ‘SensorX.sds.yml’
SDS Data Files ‘SensorX<idx0>.sds’ ‘SensorX<idx1>.sds’
data block #1
data block #2
MEMS capturing with 3,5kHz ±5%
audio signal capturing with 8kHz
Single or multiple data streams, including sensor fusion with clock deviations
  Sensors may have independent clock sources with tolerances
SDS Metadata file describes content of SDS data files
Python-based utilities for recording, playback, visualization, data conversion, and algorithm verification with off-line tools

## Slide 6: SDS Data Buffer and Record / Playback Interface
sdsio_x.c/sdsio.h Blocking R/W Interface
sdsPlay.c/h Playback Interface
sdsRec.c/h Recorder Interface
*.sds data files
SDSIO implements a blocking read/write interfaces to the communication channel that accesses the *.sds data files. Multiple SDSIO implementations are available that interface to file system, network, UART, or USB.
The Recorder and Playback application API to the application is non-blocking, thread-safe and can be called any time. to write or read data.
sds.c/h Circular Buffer Handling
A circular buffer management for each data stream triggers events back to the Recorder and Playback interface when a buffer threshold is reached.

## Slide 7: SDS Recorder https://github.com/Arm-Examples/sds-examples
Stream.csolution.yml Data streaming Reference Application for ML and DSP applications Contains several test examples (<name>.cproject.yml) and a template project with RTOS, SDS recorder control (on/off) and hooks for algorithm testing
Layer Type: SDS_Recorder Recorder Interface via Network, USB, File System
SDS Recorder
Sensor Layer Interface to I2C or SPI connected Sensor
Sensor Interface
Layer Type: Board
Existing Board Layers Provided
Board Interface
SDS Recorder contains
SDS_Rec_Network.clayer - configured for max. bandwidth
- component: SDS:Buffer
- component: SDS:IO:Socket
- component: SDS:Recorder&CMSIS-RTOS2
MDK_Network_ETH/Socket.clayer.yml
SDS_Rec_USB.clayer
- component: SDS:Buffer
- component: SDS:IO:VCOM&MDK USB
- component: SDS:Recorder&CMSIS-RTOS2
- component: USB&MDK:CORE
- component: USB&MDK:Device
- component: USB&MDK:Device:CDC

## Slide 8: Current Status of CMSIS-DSP Compute Graph
Documentation and several usage examples available today
Usage Steps with current tool flow:
  Describe the graph using Python
    Consider: No. of I/O of each node, data types, number of I/O samples produced/consumed
  Compute the optimized static scheduling from the graph (using Python)
  Generate the C++ scheduler
  Create C++ wrapper for the algorithm nodes (if they are not already available)
Signal conditioning
Filters
Echo, noise canceller
White balance
Feature extraction
Spectral data
MFCC (audio)
Convolution (pixel)
Classifier
Classical ML Deep learning (NN)
In
Out
The smarter the features, the lower the complexity of the classifier.
  More “DSP” pre-processing helps lowering the system complexity
We propose to form a working group with eco-system partners
 Video Recording of partner meeting

## Slide 9: Record real-world data with Synchronous Data Streaming (SDS)
Simplify Development of Embedded Applications that utilize DSP or ML algorithms with Sensor/Audio Input
MCU Device
Software on Physical Board
Microcontroller Hardware
SDS Recorder Interface
SDS Recorder connects via different channels
Algorithm under Development
Capture physical sensor (real-world) data using the original Microcontroller target hardware
SDS Data Files
*.gyroscope.sds
Audio Interface
Microphone Input
SDS Data Files
*.microphone.sds
z
y
x
Training Data
Validation Data
Test Data
Data conversion to ML training platform can be automated.
The SDS framework provides methods to record real-world data for analysis and development.
Input to Digital Signal Processing (DSP) development tools such as filter designers
Input to Machine Learning (ML) model classification, training, and performance optimization.
SDS framework is an open-source project: github.com/Arm-Software/SDS-Framework
MEMS Sensor Interface
Gyroscope Sensor

## Slide 10: SDS enables playback of real-world data for algorithm testing
AVH VSI
Software on Arm Virtual Hardware
Software on Physical Board
MCU Device
Combined with AVH it enables repeatable test automation in CI systems and MLOps cloud services
MEMS Sensor Interface
Gyroscope Sensor
Microcontroller Hardware
SDS Recorder Interface
SDS Recorder connects via different channels
Algorithm under Development
SDS Data Files
*.gyroscope.sds
Audio Interface
Microphone Input
SDS Data Files
*.microphone.sds
z
y
x
VSI Sensor Interface
Virtual Streaming Interface #1
Arm Virtual Hardware (AVH-FVP)
Algorithm under Development
VSI Audio Interface
Virtual Streaming Interface #2
SDS Data Files
*.gyroscope.sds
SDS Data Files
*.microphone.sds
Same algorithm is verified on precise processor simulation model

## Slide 11: SDS Data Buffer and Record / Playback Interface
Data I/O via blocking devices (fread, fwrite)
Data Recording via File I/O, STDIO, Socket
Circular Data Buffers
sds.h Circular Buffer Handling
sdsio.h Blocking R/W Interface (i.e. file I/O)
sdsRec.h Data Recording Interface
sdsPlay.h Data Playback Interface
*.sds Data Files ‘file0.sensorX.sds’ ‘file1.sensorX.sds’
Meta Info User supplied ‘sensorX.sds.yml’
Data Playback via File I/O, STDIO, Socket, or AVH VSI